Circuit Simulation in GNU/Linux
-Ashwith Jerome Rego
 ashwith@ieee.org
http://ashwith.wordpress.com

---
Revision
- Step 1?
- Schematic Capture
  - Place the components (Shortcut = i)
  - Rearrange them (Shortcut = er for rotate, ei for mirror)
  - Add nets to connect them (Shortcut = n)
  - Add attributes (Double click) – Remember to be careful here and make sure you pick the right attribute names.

---
- Step 2?
- Netlist generation
  - gnetlist -g spice-sdb -o <output>.net <input>.sch
- Step 3?
- Simulation (use -b for batch mode)
  - ngspice <netlist>.net
- View results (gaw or withing ngspice.

---
Today's Session
- Few more examples...
- Symbol creation.